## Slide 1: Robot Mapping with Proprioceptive Spatial Awareness in Confined and Sensor-Challenged Environments
Jacob Everist
Advisor: Wei-Min Shen
Committee: Ramakant Nevatia
Committee: Behrokh Khoshnevis

## Slide 2: Outline
Problem
Related Work
Approach
  sensing, features, control, robot frame, mapping
Results
Conclusion

## Slide 3: Problem
Environments that are sensor-challenged and confined are difficult to robotically explore and map
  Pipes
  Caves
External sensors such as cameras, sonar, and LIDAR may be become inoperable due to damage, occlusions, lighting and fluid conditions

## Slide 4: Environments

## Slide 5: Motivation
Allow mapping and exploration of previously inaccessible environments
  Flooded mines and caves
  Pipes and sewers
  Debris piles (INTERESTING)
Seek solution invariant to ambient fluids (air, transparent liquid, opaque liquid) (HARD)
Impacts
  Cave exploration
  Geology
  Search and rescue
  Pipe inspection (INTERESTING)

## Slide 6: Mining Disasters
West Virginia, 29 dead, 2010
Utah, 9 dead, 2007
West Virginia, 12 dead, 2006
Kentucky, 5 dead, 2006
Alabama, 13 dead, 2001

## Slide 7: Earthquakes
Haiti, 222570 dead, 2010
Sumatra, 1117 dead, 2009
Sichuan, 87587 dead, 2008
Peru, 514 dead, 2007
Java, 5749 dead, 2006
Pakistan, 80361 dead, 2005
Sumatra, 227898 dead, 2004
Iran, 31000 dead, 2003

## Slide 8: Cave Exploration

## Slide 9: Utility Inspection

## Slide 10: Rediscover Old Infrastructure

## Slide 11: Major Challenges
  Variant fluids
  Void space detection
    Large chambers vs. slip of anchors
  Reflections, distortions
  Dark
  Unstructured environment
  Loose debris
  Variable wall widths
  No odometry or dead-reckoning
  No GPS

## Slide 12: Related Work
Mapping underground mines [Thrun04]
Pipe inspection [Fukuda89]
Flooded subterranean caves [Gary08]
Robot sub under sea ice [Kunz et al 08]
Geometric contact detection [Kaneko94], [Grupen, Huber93], [Haidacher02], [Mimura94]
Probing the boundary in an oil well [Mazzini11]
Initial work sensing void space [Everist09]

## Slide 14
Wheels

## Slide 15
Wheels
Sonar

## Slide 16
Wheels
Sonar
LADAR

## Slide 17
Wheels
Sonar
LADAR
Vision

## Slide 19
Incompatible Mobility

## Slide 20
No Odometry

## Slide 21
Failure by Proximity

## Slide 22
Failure by Ambient Fluid

## Slide 23: Approach
Algorithmic methods for robotically mapping
  confined environments
  proprioceptive sensors only
Use an articulated mobile robot
  Use joint sensors and geometry to reconstruct robot posture
  The robot should have many joints, known geometry, and a far reach
Use robot posture to identify void space
  Sweep the body to build up information
  Boundaries are indirectly inferred from mapped void space

## Slide 25: Assumptions
Robot
  All external sensors have failed
  Only joint angle sensors are available
  Dynamically set max torque
  Body geometry is known
Environment
  Confined
  Pipe-like or tubular
  Rigid walls
  Flat ground, no slopes
  Variable width (map and navigate)
  Constant width (map, navigate, w/ junctions)
Simulation Only
  Rigid Body Physics Engine
  Bullet Physics: https://github.com/bulletphysics/

## Slide 26: Evaluation
Success metric:
  Can the robot generate a map of the environment?
  Can the map be used by other robots for navigation?
Task:
  Use the robot the explore and generate the map
  Give the map to a new robot, direct it to a location on the map
  Does it reach the target location?

## Slide 27
Sensing
Features
Robot Frame
Control
Build Maps
Junctions
Max Likelihood Map

## Slide 28: External Sensor Failure

## Slide 29: Types of Sensing
Concepts from biology
Exteroception
  sight, hearing, touch, taste, smell
Proprioception
  relative position of neighboring parts of the body
  strength of effort
Interoception
  hunger, hot, cold, thirst, pain, etc.

## Slide 30: Sensing with Proprioception
Obstacle detection is standard approach for mapping methods.
  Use external sensors to detect boundaries
With proprioception only, using various contact detection strategies, we can get some boundary detection.
Existing methods:
  contact detection (infer contact from geometry)
  finger probing (detailed point contacts)

## Slide 31: Sensing Void Space
Problem: without external sensors, how do we sense the environment with proprioception?
Solution: Build maps of void space using the robot’s body to sweep out the space
Inference of the boundary from shape of void space
  Tells you where obstacle are not, not where they are

## Slide 32: Proprioceptive Spatial Awareness
Use movement and body geometry to build awareness of space
Plot into a local map representing void space

## Slide 37: Proprioceptive Sensing
The posture image It , is captured at pose Xt by sweeping the body in one direction and anchoring in the other direction.

## Slide 38
Sensing Void Space
Position and Orientation
Control and Locomotion
Environmental Landmarks and Features
Building Maps
Mapping with Junctions
Probabilistic Mapping

## Slide 39: Environmental Landmarks and Features
In order localize the robot and build a map, we need some features of the environment to exploit
Candidates include:
  Obstacles/walls
  Corners
  Shape features
  Spatial features
    bloom, arch, bend

## Slide 40: Shape Features
Given a blob of void space, what properties can we extract?
Shape of the robot’s posture in space should give us information about the environment.
How can we extract this information and represent it in an useful way?

## Slide 41: Shape Feature
“Spatial Curve”
Smoothed version gives us a curve representation of the space
Union of multiple void space images with medial axis give us graph representation of environment topology

## Slide 42
Spatial curve from Posture image
ct = scurve(It)

## Slide 44: Spatial Features
We detect 3 different spatial feature from spatial images that are indicate of junctions:
  blooms: swelling at the tip (CONSTANT WIDTH)
  arches: internally swelling, “arched” anchors (CONSTANT WIDTH)
  bends: sudden turn of spatial curve, crest is the bend point (DYNAMIC WIDTH)
Using these landmark features, we now include proximity with each other in the evaluation of motion estimation, branch state, and pose localization.
Using this approach, we are able to map and align the arms of a T and cross junction with ease.
The addition of the spatial features makes mapping and aligning the other junction much more rapid.

## Slide 47
Width

## Slide 48
Sensing Void Space
Position and Orientation
Control and Locomotion
Environmental Landmarks and Features
Building Maps
Mapping with Junctions
Probabilistic Mapping

## Slide 49: Robot Frame
Articulated robot has no high-inertia center of mass to serve as its coordinate frame.
  Individual segments are rotating and undulating
Need method to determine direction of snake robot.
  Information not provided by individual body segments

## Slide 51: Posture Curve
Robot-centered Coordinate Frame
dynamically generated from B-spline
“Posture Curve” generated by smoothed B-spline with segment frame origins as input points (example)
Generates the Posture Frame for local coordinate system

## Slide 54
Sensing Void Space
Position and Orientation
Control and Locomotion
Environmental Landmarks and Features
Building Maps
Mapping with Junctions
Probabilistic Mapping

## Slide 55: Control and Locomotion
Simulated robot control
Concertina locomotion
Snake control, backbone curves (Chirikjian)
Segmented behaviors
Adaptive anchoring
Smooth motion and compliance
Stability detection

## Slide 56: Concertina Motion
Gans 1980

## Slide 57: Gait Stages
Rest-State
Front-Extend
Front-Anchor
Back-Extend
Back-Anchor
Rest-State

## Slide 58
Sensing Void Space
Position and Orientation
Control and Locomotion
Environmental Landmarks and Features
Building Maps
Mapping with Junctions
Probabilistic Mapping

## Slide 59: Inputs
Locomotion Step
Posture Image
Pose

## Slide 60: Initial Condition for Building the Map
Poses X1 =(0,0,0) and X2 = ?
Forward sweep I1 and backward sweep I2
Raw images
GPAC images, hull and spatial curve

## Slide 61: 4 Methods
Naive Approach
Axis Method
Junction Method
Probabilistic Method

## Slide 62: In-Place Constraint
overlap spatial curves of X1 and X2
C1 = scurve(I1)
C2 = scurve(I2)
X2 = overlap(X1, C1, C2, d=0)
Generalized ICP algorithm to fit
Image of in-place fit

## Slide 64: Step Constraint
X_3 and X_4 are new poses after locomotion step
Solve for new location through “step constraint”
X_3 = overlap(X_1, I_1, I_3, d=+\delta)
\delta = 0.5/0.8 ?
Constant \delta is the estimated distance traveled
Image of step ICP fit

## Slide 67: Shortcoming of Naive Approach
Only consistent with last pose
  history is ignored
Poses can flair off path
Backtracking
  does not stay on past path

## Slide 68: Axis Constraint
Compute union of past poses’ posture images
Compute medial axis of the map
New pose must constrain to existing axis
Image of union, medial axis
Image of pose constraint to axis

## Slide 71: Process of Axis Approach
apply step constraint to make initial estimated pose
apply axis constraint around estimated pose
Image initial guess
Image snap to axis

## Slide 72: Mapping Problem (backup)
Actions:
  Move commands:
Sensing:
  Posture sequence:
  Posture Images:
Map Parameters:
  Poses:

## Slide 73
Sensing Void Space
Position and Orientation
Control and Locomotion
Environmental Landmarks and Features
Building Maps
Mapping with Junctions
Probabilistic Mapping

## Slide 74: Problem
Axis constraint mapping does not work in environments with junctions
Does not correctly fit to axis with ICP

## Slide 75: Curve Events
Contained
Extending
Divergent

## Slide 76: Branching
Branching event
Create two axes (skeletons now)
No longer a single curve, but a tree (skeleton)

## Slide 79: Localization on Skeletons
No longer curve-to-curve ICP
ICP to multiple skeletons
Multiple configurations

## Slide 80: Localization Process (how to fit a new pose into past set of skeletons)
Collect set of skeleton terminals
Disregard terminals that are similar or subsumed by another skeleton
Collect (n choose 2) paths between each pair of n terminals
Perform ICP on each spliced path
Evaluate and select “best fit” according to some criteria
DEFINE “SPLICES”

## Slide 83: Branch Detection
Given a new pose’s spatial curve, is it branching?
spatial curve is diverging from axis
distance of tip from nearest point on axis is greater than D
other criteria?

## Slide 84: Mapping Process
Locomotion Step
Capture Posture Images
Estimate new pose with step constraint
Determine if it branches
  add pose to skeleton
Localize new pose to each splice
Select best fit

## Slide 85
Sensing Void Space
Position and Orientation
Control and Locomotion
Environmental Landmarks and Features
Building Maps
Mapping with Junctions
Probabilistic Mapping

## Slide 86: Problems
Branching in right location?
New branch, existing branch, or no branch?
Pose in right location?
Leads to a probabilistic method

## Slide 87: Approach
Sample many poses
Sample many spatial relations between skeletons
Select maximum likelihood state as our map

## Slide 88: Parameterization
Possible poses of the new posture image
Skeleton sets: Grouping of all posture image with pose information
Spatial relationship between skeletons

## Slide 89: Spatial Transform of Skeletons
Control point on “parent” skeleton
Reduced to 1D parameter space

## Slide 92: Mapping Problem
Actions:
  Move commands:
Sensing:
  Posture vector: snapshot of joints time t
  Posture sequence: series of snapshots from sweep behavior
  Posture Images: union of robot’s geometry under posture sequence
Map Parameters:
  Poses:
  Skeletons:
  Control Points:

## Slide 93: Motion Estimation
Sample possible poses uniformly along all splices of the set of overlapping skeletons
Evaluate based on consistency F(x)
Bias likelihood with Gaussian curve representing motion estimated from last best pose
Select best possible pose, keep all past sampled possible poses

## Slide 96: Add to Map
Determine if pose’s spatial curve is diverging
Create new branching skeleton if diverging
Otherwise, add to an existing skeleton

## Slide 97: Branching State
Evaluate all branch states
Maximize evaluation function G(T1,T2)
  Measures overlap and landmark consistency

## Slide 98: Localization
ICP localize all previous samples across all splices
Select maximum evaluated pose H(x)
Correct map the map with max likelihood pose

## Slide 99: Merge
Merge skeletons together if they are fully constrained

## Slide 106
 | T Junction from Bottom | T Junction from Side | Y junction | Right L-junction | Left L-junction | Cross Junction | Straight Pipe | Irregular Pipe | Right 60-junction | Left 60-junction
Forward Locomotion |  |  |  |  |  |  |  |  |  | 
Backtracking |  |  |  |  |  |  |  |  |  | 
Single Junction |  |  |  |  |  |  |  |  |  | 
Multi-Junctions |  |  |  |  |  |  |  |  |  | 
Navigation |  |  |  |  |  |  |  |  |  | 
Legend |  |  |  |  |  |  |  |  |  | 
Success |  |  |  |  |  |  |  |  |  | 
Partial Success |  |  |  |  |  |  |  |  |  | 
Not yet demonstrated |  |  |  |  |  |  |  |  |  | 
N/A |  |  |  |  |  |  |  |  |  | 

## Slide 107: Results
Y_junc: S S C
T_bottom: S S C
T_side: S S S
cross: S S S
60-right: S S S
60-left: S S S
L-right: S S S
L-left: S S S
Straight: S S S
Irregular: S S S
S = success, C = crash

## Slide 109: Contributions
Use proprioceptive sensors to map
Use void space to build a map
Map representation using posture images, poses, and overlapping skeletons
Sensing the environment through joint sensors, no contact, vision, or range sensors. First method without exteroception (IROS2009)
Map the environment with no fixed reference frame. Mobile platform
New map representation for confined, tubular, void spaces
  Operates without landmark features
  Uses holistic shape of the environment
  Localization by ICP over medial axes of shapes
Mapping with only highly local information
  no sensing at a distances
Detection of junctions that are only partially observable in non-looped environment
Probabilistic representation over space of possible maps
Can map Y junctions, T junctions, X junctions, L and 45deg junctions in non-looping environments
Proprioceptive odometer/dead-reckoning (self-posture motion model)

## Slide 110: Conclusion
We developed a method of mapping confined environments when external sensors are not available
We use proprioceptive sensors and the robot’s known geometry
We were able to explore, map and navigate environments with a variety of features in a simulated environment

## Slide 111: Challenges
Drift
Length
Loops

## Slide 112: Future Work
3D environments
Physical robots
Different type’s of robots
Loose clutter in environment
Switch off between external and proprioceptive
Large-scale environments
Environments with loops