## Slide 1: Robot Mapping with Proprioceptive Spatial Awareness in Confined and Sensor-Challenged Environments
Jacob Everist
Advisor: Wei-Min Shen
Committee: Ramakant Nevatia
Committee: Behrokh Khoshnevis

## Slide 2: Outline
Problem
Related Work
Approach
  sensing, features, control, robot frame, mapping
Results
Conclusion

## Slide 3: Problem
Environments that are sensor-challenged and confined are difficult to robotically explore and map
  Pipes
  Caves
External sensors such as cameras, sonar, and LIDAR may be become inoperable due to damage, occlusions, lighting and fluid conditions

## Slide 4: Environments

## Slide 5: Motivation
Allow mapping and exploration of previously inaccessible environments
  Flooded mines and caves
  Pipes and sewers
  Debris piles (INTERESTING)
Seek solution invariant to ambient fluids (air, transparent liquid, opaque liquid) (HARD)
Impacts
  Cave exploration
  Geology
  Search and rescue
  Pipe inspection (INTERESTING)

## Slide 6: Mining Disasters
West Virginia, 29 dead, 2010
Utah, 9 dead, 2007
West Virginia, 12 dead, 2006
Kentucky, 5 dead, 2006
Alabama, 13 dead, 2001

## Slide 7: Earthquakes
Haiti, 222570 dead, 2010
Sumatra, 1117 dead, 2009
Sichuan, 87587 dead, 2008
Peru, 514 dead, 2007
Java, 5749 dead, 2006
Pakistan, 80361 dead, 2005
Sumatra, 227898 dead, 2004
Iran, 31000 dead, 2003

## Slide 8: Cave Exploration

## Slide 9: Utility Inspection

## Slide 10: Rediscover Old Infrastructure

## Slide 11: Major Challenges
  Variant fluids
  Void space detection
    Large chambers vs. slip of anchors
  Reflections, distortions
  Dark
  Unstructured environment
  Loose debris
  Variable wall widths
  No odometry or dead-reckoning
  No GPS

## Slide 12: Related Work
Mapping underground mines [Thrun04]
  Large space, able to use range sensors, easy mobility
Pipe inspection [Fukuda89]
  evacuated tubes, external sensors operable
Flooded subterranean caves [Gary08]
  calibrated sonar, large space
Robot sub under sea ice [Kunz et al 08]
  calibrated sonar, large space
Geometric contact detection [Kaneko94], [Grupen, Huber93], [Haidacher02], [Mimura94]
  non-mobile, high accuracy, time-consuming
Probing the boundary in an oil well [Mazzini11]
  non-mobile, high accuracy, time-consuming
Initial work sensing void space [Everist09]
  preliminary work

## Slide 14
Wheels

## Slide 15
Wheels
Sonar

## Slide 16
Wheels
Sonar
LADAR

## Slide 17
Wheels
Sonar
LADAR
Vision

## Slide 19
Incompatible Mobility

## Slide 20
No Odometry

## Slide 21
Failure by Proximity

## Slide 22
Failure by Ambient Fluid

## Slide 23: Approach
Algorithmic methods for robotically mapping
  confined environments
  proprioceptive sensors only
Use an articulated mobile robot and reconstruct posture
  Use joint sensors and geometry to reconstruct robot posture
  The robot should have many joints, known geometry, and a far reach
Use robot posture to identify void space
  Sweep the body to build up information
  Boundaries are indirectly inferred from mapped void space

## Slide 25: Assumptions
Robot
  All external sensors have failed
  Only joint angle sensors are available
  Dynamically set max torque
  Body geometry is known
Environment
  Confined
  Pipe-like or tubular
  Rigid walls
  Flat ground, no slopes
  Variable width (map and navigate)
  Constant width (map, navigate, w/ junctions)
Simulation Only
  Rigid Body Physics Engine
  Bullet Physics: https://github.com/bulletphysics/

## Slide 26: Evaluation
Success metric:
  Can the robot generate a map of the environment?
  Can the map be used by other robots for navigation?
Task:
  Use the robot the explore and generate the map
  Give the map to a new robot, direct it to a location on the map
  Does it reach the target location?

## Slide 27
Search for Best Map
Junctions
Build Maps
Control
Robot Frame
Features
Sensing

## Slide 28: External Sensor Failure

## Slide 29: Types of Sensing
Concepts from biology
Exteroception
  sight, hearing, touch, taste, smell
Proprioception
  relative position of neighboring parts of the body
  strength of effort
Interoception
  hunger, hot, cold, thirst, pain, etc.

## Slide 30: Sensing with Proprioception
Obstacle detection is standard approach for mapping methods.
  Use external sensors to detect boundaries
With proprioception only, using various contact detection strategies, we can get some boundary detection.
Existing methods:
  contact detection (infer contact from geometry)
  finger probing (detailed point contacts)

## Slide 31: Sensing Void Space
Problem: without external sensors, how do we sense the environment with proprioception?
Solution: Build maps of void space using the robot’s body to sweep out the space
Inference of the boundary from shape of void space
  Tells you where obstacle are not, not where they are
Extract maximum information from minimal sensors

## Slide 32: Proprioceptive Spatial Awareness
Use movement and body geometry to build awareness of space
Plot into a local map representing void space

## Slide 37: Proprioceptive Sensing
The posture image It , is captured at pose Xt by sweeping the body in one direction and anchoring in the other direction.

## Slide 38
Search for Best Map
Junctions
Build Maps
Control
Robot Frame
Features
Sensing

## Slide 39: Environmental Landmarks and Features
Features to build the map
Boundary features
  Obstacles/walls
  Corners
Void space features
  Shape features
  Spatial features

## Slide 40: Shape Features
Shape of the sensed void space in local environment should give us information.
How can we extract this information and represent it in an useful way?

## Slide 41: Shape Feature
Spatial curve ct = scurve(It) where It is posture image
Smoothed version gives us a curve representation of the local space

## Slide 42
Spatial curve ct from posture image It
ct = scurve(It)
Posture Image It

## Slide 43: Spatial Features
3 different spatial features from posture images
  blooms
  arches
  bends
Landmarks usually indicate junctions or gaps in space
Can match landmarks together to improve the map

## Slide 44
Curve Length
Curve Length
Width
Tangent
Angle
  Blooms: swelling at the tip (assumes constant width)

## Slide 45
Curve Length
Curve Length
Width
Tangent
Angle
  Arches: internal swelling, “arched” anchors (assumes constant width)

## Slide 46
Curve Length
Curve Length
Width
Tangent
Angle
  Bends: sudden turn of spatial curve, crest is the bend point (permits dynamic width)

## Slide 47
Search for Best Map
Junctions
Build Maps
Control
Robot Frame
Features
Sensing

## Slide 48: Robot Frame
Articulated robot has no high-inertia center of mass to serve as its coordinate frame.
  Individual segments are rotating and undulating
Need method to determine direction of snake robot.
  Information not provided by individual body segments

## Slide 49: Posture Curve
Posture curve generated by smoothed B-spline with joint locations as inputs
Generates the posture frame for local coordinate system
Different from spatial curve which represents local sensed environment

## Slide 50
Body Frame B
Posture Frame P
Global Frame G
Posture Curve
Pose of Frame P in Frame G
XG = (x, y, θ)

## Slide 51
Search for Best Map
Junctions
Build Maps
Control
Robot Frame
Features
Sensing

## Slide 52: Control and Locomotion
Simulated robot control
  algorithms tuned for simulated environment
Concertina locomotion
  Practical heuristic for sensor-deprived environment
Snake control, backbone curves (Chirikjian)
  inverse kinematics by fitting to a curve
Segmented behaviors
  sections of linkage controlled by different behaviors
Adaptive anchoring
  making strong and stable anchors to the walls with verification
Smooth motion and compliance
  interpolated and compliant motion
Stability detection
  checking for slip and transient disturbances

## Slide 53: Concertina Motion
Gans 1980

## Slide 54: Gait Stages
Rest-State
Front-Extend
Front-Anchor
Back-Extend
Back-Anchor
Rest-State

## Slide 55
Search for Best Map
Junctions
Build Maps
Control
Robot Frame
Features
Sensing

## Slide 56: Inputs
Locomotion Step
Posture Image
Pose

## Slide 57: Initial Condition for Building the Map
Poses X1 =(0,0,0) and X2 = ?
Forward sweep I1 and backward sweep I2
Spatial curves C1 = scurve(I1), C2 = scurve(I2)
I2
I1
C2
C1

## Slide 58: 4 Methods
Naive Method
Axis Method
Junction Method
Search Method

## Slide 59: In-Place Constraint
overlap spatial curves of X1 and X2
X2 = overlap(X1, C1, C2, d=0)
Generalized Iterative Closest Point (genICP) algorithm to fit

## Slide 60: Step Constraint
X3 and X4 are new poses after locomotion step
Solve for new location
X3 = overlap(X1, C1, C3, d=δ) where δ = 0.5
Constant δ is estimated distance traveled giving initial guess

## Slide 62: Shortcoming of Naive Method
Only consistent with last pose
  history is ignored
Poses can flair off path
Backtracking
  does not stay on past path

## Slide 63: Axis Method
Compute union of past poses’ posture images
Compute medial axis of the map
New pose must constrain to existing axis

## Slide 64: Steps of Axis Method
apply step constraint to make initial estimated pose
apply axis constraint around estimated pose

## Slide 65
Search for Best Map
Junctions
Build Maps
Control
Robot Frame
Features
Sensing

## Slide 66: Problem
Axis constraint mapping does not work in environments with junctions
Does not correctly fit to axis with ICP

## Slide 67: Skeleton
The medial axis of the union of posture images with pose information

## Slide 68: Branching
Look for cases where spatial curve branches off the existing skeleton
Create a new skeleton

## Slide 69: Define Curve Events
Contained
Extending
Divergent

## Slide 72: Localization on Skeletons (Junction Method)
No longer curve-to-curve ICP
ICP to multiple skeletons
Multiple configurations
Create splices on sets of overlapping skeletons
Defined by a path between any two skeleton terminals

## Slide 75: Fit a New Pose onto Past Skeletons (Junction Method)
Collect set of skeleton terminals
Disregard terminals that are similar or subsumed by another skeleton
Collect (n choose 2) paths between each pair of n terminals
Perform ICP on each spliced path
Evaluate and select “best fit” according to some criteria

## Slide 76
Search for Best Map
Junctions
Build Maps
Control
Robot Frame
Features
Sensing

## Slide 77: Problems
Branching in right location?
New branch, existing branch, or no branch?
Pose in right location?
Leads to a search method

## Slide 78: Search Method
Sample many poses
Sample many spatial relations between skeletons
Select best evaluated state as our map

## Slide 79: Parameterization
Possible poses of the new posture image Xt
Skeleton sets: Grouping of all posture image with pose information Sk
Spatial relationship between skeletons bk

## Slide 80: Mapping Problem
Actions:
  Move commands:
Sensing:
  Posture vector: snapshot of joints time t
  Posture sequence: series of snapshots from sweep behavior
  Posture Images: union of robot’s geometry under posture sequence
Map Parameters:
  Poses:
  Skeletons:
  Control Points:

## Slide 81: Spatial Transform of Skeletons
Control point on “parent” skeleton
Reduced to 1D parameter space

## Slide 84: Search Method
Solve best fit for Xt, skeletons S1:k, and spatial relation b1:k
Motion Estimation
Add-to-Skeletons
Overlap Skeletons
Localize Pose to Map
Merge Skeletons

## Slide 85: Motion Estimation
Sample possible poses uniformly along all splices of the set of overlapping skeletons
Evaluate based on consistency F(x)
  F(x) = -2*overlapSum0 – 2*overlapSum1 – angDiff0/Pi – angDiff1/Pi + 2*normLandmarkSum
Bias likelihood with Gaussian curve representing motion estimated from last best pose
Select best possible pose, keep all past sampled possible poses

## Slide 88: Add to Map
Determine if pose’s spatial curve is diverging
Create new branching skeleton if diverging
Otherwise, add to an existing skeleton

## Slide 89: Skeletons Overlapping State
Evaluate all skeleton states
Maximize evaluation function G(b12)
  Measures overlap and landmark consistency
  G(b12) = normLandmarkCost * normMatchCount

## Slide 90: Localization
ICP localize all previous samples across all splices
Select maximum evaluated pose H(x)
  H(x) = normLandmarkSum * contigFrac0 * contigFrac1
Correct the map with best fit pose

## Slide 93: Merge
Merge skeletons together if they are fully constrained

## Slide 94: Experimental Results

## Slide 95: Experimental Setup
  Bullet Physics: https://github.com/bulletphysics/
  Amazon EC2 Cloud
  c3.8xlarge provisioned server (32 vCPUs, 60GiB memory)
  time taken = ?
  money cost = ~ $1000

## Slide 96
Capabilities | Forward | Backtracking | Junctions | Navigation
60_right | S | S | S | S
60_left | S | S | S | S
L_right | S | S | S | S
L_left | S | S | S | S
Y | S | S | S | S
T_bottom | S | S | S | S
T_side | S | S | S | S
cross | S | S | S | S
Capabilities
S = success, X = not capable

## Slide 97: Results
S = success, X = crash
Results | 0.0 | 0.2 | 0.4
60_right | S | S | S
60_left | S | S | S
L_right | S | S | S
L_left | S | S | S
Y | X | S | S
T_bottom | S | S | X
T_side | S | S | S
cross | S | S | S

## Slide 105: Conclusion

## Slide 106: Contributions
Use proprioceptive sensors only to map
Use void space to build a map
Map representation using posture images, poses, and overlapping skeletons
Mobile platform mapping
Articulated robot mapping
Junctions in non-looping environment

## Slide 107: Conclusion
We developed a method of mapping confined environments when external sensors are not available
We use proprioceptive sensors and the robot’s known geometry
We were able to explore, map and navigate environments with a variety of features in a simulated environment

## Slide 108: Future Work
Angular drift
Straight featureless pipes
Environments with loops
3D environments
Physical robots
Different type’s of robots
Loose clutter in environment
Switch off between external and proprioceptive
Large-scale environments

## Slide 109: End

## Slide 110: Mapping Problem (backup)
Actions:
  Move commands:
Sensing:
  Posture sequence:
  Posture Images:
Map Parameters:
  Poses: