## Slide 1: Robot Mapping with Proprioceptive Spatial Awareness in Confined and Sensor-Challenged Environments
Jacob Everist

## Slide 2: Problem
Environments that are sensor-challenged and confined are difficult to robotically explore and map
  Pipes
  Caves
External sensors such as cameras, sonar, and LIDAR may be become inoperable due to damage, occlusions, lighting and fluid conditions

## Slide 3: Environments

## Slide 4: Motivation
Allow mapping and exploration of previously inaccessible environments
  Flooded mines and caves
  Pipes and sewers
  Debris piles
Seek solution invariant to ambient fluids (air, transparent liquid, opaque liquid)
Impacts
  Cave exploration
  Underground science
  Search and rescue
  Pipe inspection

## Slide 5: Mining Disasters
West Virginia, 29 dead, 2010
Utah, 9 dead, 2007
West Virginia, 12 dead, 2006
Kentucky, 5 dead, 2006
Alabama, 13 dead, 2001

## Slide 6: Earthquakes
Haiti, 222570 dead, 2010
Sumatra, 1117 dead, 2009
Sichuan, 87587 dead, 2008
Peru, 514 dead, 2007
Java, 5749 dead, 2006
Pakistan, 80361 dead, 2005
Sumatra, 227898 dead, 2004
Iran, 31000 dead, 2003

## Slide 7: Cave Exploration

## Slide 8: Utility Inspection

## Slide 9: Rediscover Old Infrastructure

## Slide 10: Related Work
Mapping underground mines [Thrun04]
Pipe inspection [Fukuda89]
Flooded subterranean caves [Gary08]
Robot sub under sea ice [Kunz et al 08]
Geometric contact detection [Kaneko94], [Grupen,Huber 93], [Haidacher02], [Mimura94]
Probing the boundary in an oil well [Mazzini11]
Initial work sensing void space [Everist09]

## Slide 11: Related Work (overview)
SLAM
Underground Mapping
Pipe Inspection
Tactile Sensing
Geometric Probing
Contact Detection
Snake Robots
Pigging

## Slide 12: Related Work (1)
SLAM
  (Cheeseman 1986)
  (Durrant-Whyte 1991)
Underground Mapping
  Mines (Thrun 2003)
  Sink holes (Gary 2008)
  Ice lakes (Stone Aerospace 2010)
Pipe Inspection
  Wheels, treads, walkers, snakes
    (Fukuda 1989)
    (Kawaguchi 1995)
    (Suzumori 1999)
    (Wakimoto 2003)

## Slide 13: Related Work (2)
Tactile Sensing
  Whiskers (Russell 1992)
  Bump sensors
  Tactile surfaces (Liu 2003)
  Shape classification (Erdmann 2001)
Geometric Probing
  Polygon reconstruction (Skiena 1988)
Contact Detection
  2D (Grupen 1994)
  3D (Kaneko 1995)

## Slide 14: Related Work (3)
Snake Robots
  Biomechanics (Hirose 1974)
  Control (Chirikjian 1995)
  Design (Choset 2007)
Pigging
  “Pipeline Pigging Technology” (Tiratsoo 1992)

## Slide 15: Existing Approach

## Slide 17
Wheels

## Slide 18
Wheels
Sonar

## Slide 19
Wheels
Sonar
LADAR

## Slide 20
Wheels
Sonar
LADAR
Vision

## Slide 22
Incompatible Mobility

## Slide 23
No Odometry

## Slide 24
Failure by Proximity

## Slide 25
Failure by Ambient Fluid

## Slide 26: Major Challenges
Sensing
  Variant fluids
  Reflections, distortions
  Dark
Movement
  Unstructured environment
  Debris, caves
  Wall widths
Motion Estimation
  No odometry or dead-reckoning
  No GPS

## Slide 27: Approach
Algorithmic methods for robotically mapping
  confined environments
  proprioceptive sensors only
Use an articulated mobile robot
  Use joint sensors and geometry to reconstruct robot posture
  The robot should have many joints, known geometry, and a far reach
Use robot posture to identify void space
  Sweep the body to build up information
  Boundaries are indirectly inferred from mapped void space

## Slide 29: Assumptions
Robot
  All external sensors have failed
  Only joint angle sensors are available
  Set max torque or current
  Body geometry is known
Environment
  Confined
  Pipe-like or tubular
  Rigid walls
  Flat ground, no slopes

## Slide 31: Evaluation
Success metric:
  Can the robot generate a map of the environment?
  Can the map be used by robots for navigation?
Task:
  Use the robot the explore and generate the map
  Give the map to a new robot, direct it to a location on the map
  Does it reach the target location?

## Slide 32: Contributions
Sensing the environment through joint sensors, no contact, vision, or range sensors. First method without exteroception (IROS2009)
Map the environment with no fixed reference frame. Mobile platform
New map representation for confined, tubular, void spaces
  Operates without landmark features
  Uses holistic shape of the environment
  Localization by ICP over medial axes of shapes
Mapping with only highly local information
  no sensing at a distances
Detection of junctions that are only partially observable in non-looped environment
Probabilistic representation over space of possible maps
Can map Y junctions, T junctions, X junctions, L and 45deg junctions in non-looping environments
Proprioceptive odometer/dead-reckoning (self-posture motion model)

## Slide 33: Outline
Sensing Void Space
Position and Orientation
Control and Locomotion
Motion Estimation
Environmental Landmarks and Features
From Poses to Maps
Mapping with Junctions
Probabilistic Mapping

## Slide 35: Sensing with Proprioception
Obstacle detection is standard approach for mapping methods.
  Use external sensors to detect boundaries
With proprioception only, using various contact detection strategies, we can get detail, sparse, or implicit boundary detection

## Slide 36: Contact Detection
Brushing objects with compliant joints and deliberate actions
Gives detailed boundary information.
  time-consuming and not well suited to long-range exploration
  primarily for detailed exploration of small space
  Kaneko, Haidacher, Grupen

## Slide 37: Finger-Probing
Poke the wall with the head of a finger or snake
When head ceases motion, this becomes “contact”
More sparse data
  prone to noise
  lots of false positives

## Slide 38: Void Space
Inference of the boundary from shape of void space
  Tells you where obstacle are not, not where they are

## Slide 39: Sensing Void Space
Problem: in the event of failure of external sensors, how do we sense the environment with proprioception?
Solution: Build maps of void space using the robot’s body to sweep out the space

## Slide 40: Proprioceptive Spatial Awareness
Use movement and body geometry to build awareness of space
Plot into a local map representing void space

## Slide 41: External Sensor Failure

## Slide 46: Probing the Environment

## Slide 47: Free Space Map

## Slide 48: Sensing Requires Reference
Anchoring provides global frame
Bad references cause “bowtie effect”

## Slide 49: Free Space

## Slide 50: Free Space
gap in free space

## Slide 51: Free Space
gap in free space
smooth out these gaps

## Slide 52: Free Space Smoothing
Alpha shape (Edelsbrunner 1983)
  Generalization of convex hull

## Slide 53: Free Space Smoothing
Alpha shape (Edelsbrunner 1983)
  Generalization of convex hull
Input:
  Set of points
  Circle radius r

## Slide 54: Free Space Smoothing
Alpha shape (Edelsbrunner 1983)
  Generalization of convex hull
Input:
  Set of points
  Circle radius r
If some circle C has points p and q on boundary and C contains no other points

## Slide 55: Free Space Smoothing
Alpha shape (Edelsbrunner 1983)
  Generalization of convex hull
Input:
  Set of points
  Circle radius r
If some circle C has points p and q on boundary and C contains no other points
  Add edge between p and q

## Slide 56: Examples

## Slide 57: Free Space Smoothing

## Slide 58: Free Space Smoothing
gap smoothed over

## Slide 59: Free Space Smoothing
gap smoothed over
sharp features lost

## Slide 60: Proprioceptive Sensing
The posture image It , is captured at pose Xt by sweeping the body in one direction and anchoring in the other direction.

## Slide 61: Defining Position and Orientation
Articulated robot has no high-inertia center of mass to serve as its coordinate frame.
  Individual segments are rotating and undulating
Need method to determine direction of snake robot.
  Information not provided by individual body segments

## Slide 62: Approach
Robot-centered Coordinate Frame
dynamically generated from B-spline
Backbone Curve defined by Chirikjian (example)
“Posture Curve” generated by smoothed B-spline with segment frame origins as input points (example)
Generates the Posture Frame for local coordinate system

## Slide 68: Control and Locomotion
Not major contribution because not implemented on physical robot.
Concertina locomotion
Snake control, backbone curves (chirikjian)
Segmented behaviors
Adaptive anchoring
Smooth motion and compliance
Stability detection

## Slide 69: Snake Locomotion

## Slide 70: Concertina Motion
Gans 1980

## Slide 71: Adaptive Concertina Gait
Variable width pipes
No tactile sensors

## Slide 72: Segmented Behavioral Control

## Slide 73: Snake Control
Sine curves with configurable amplitudes per period
Backbone curve fitting (Chirikjian 1995)
Adaptive anchoring

## Slide 74: Gait Stages
Rest-State
Front-Extend
Front-Anchor
Back-Extend
Back-Anchor
Rest-State

## Slide 75: New Ideas
Adaptive snake robot locomotion with a version of concertina gait
Detect anchoring with joint sensors

## Slide 80: Environmental Landmarks and Features
In order localize the robot and build a map, we need some features of the environment to exploit
Candidates include:
  Obstacles/walls
  Corners
  Shape features
  Spatial features
    bloom, arch, bend

## Slide 81: Corner Detection
Hypothesis: find corner features in void space image and use them as mapping features
Corner in void space image implies a junction
Assumes junctions have sharp corners. Smoothed corners need not apply.
High false positive rate
Serendipitous detection of actual corners
Frequent misses or reject by algorithm
Better suited to sensors that measure complete boundary, not incomplete boundary

## Slide 82: Shape Features
Given a blob of void space, what properties can we extract?
Shape of the robot’s posture in space should give us information about the environment.
How can we extract this information and represent it in an useful way?

## Slide 83: Shape Features
3 options
  Anchor Curves:
    Anchor points, create smoothed boundary
  Wall Curves:
    Alpha shape, polygon boundaries
  Spatial Curve:
    Medial axis or “skeletonization” (cite)
3 example images

## Slide 84: Spatial Curve
Smoothed version gives us a curve representation of the space
Union of multiple void space images with medial axis give us graph representation of environment topology

## Slide 87: Spatial Features
Bloom
Arch
Bend

## Slide 88: Motion Estimation
Self-Posture motion model
  slow time
  high accuracy
Naive motion model
  fast time
  low accuracy
Step model with inter-pose overlap invariance
  fast time
  medium accuracy
Shoot step
  fast time
  medium accuracy

## Slide 89: Self-Posture Motion Model
How do we estimate the change in pose as a result of a locomotion step?
  Anchoring approach
  kinematically track fixed points in the environment during locomotion
  requires that reference poitns are sufficiently stable
  does not slip, wobble, etc. (anchor failure modes)
  high accuracy but costly in time, slow-moving
  in event of slip, high rotational error
  high cost, high reward, catastrophic error possible
  not good enough (multi-day simulations)

## Slide 90: Naive Inter-Pose Step
Pose A and pose B between locomotion step
Displace a fixed distance along spatial curve
  (graphic here)
Possible bus has high error since the two poses don’t always overlap
Fast to compute though

## Slide 91: Overlap Inter-Pose Step
Extend the naive step
Recognize that consecutive poses overlap each other
  assume invariant condition
Perform the naive step displacement
Perform Iterative Closest Point (ICP) between two curves to find best fit
ICP details:
  Generalized ICP (cite)
  covariance matrices with Mahalanobis distance cost
  extra details that keep partial overlap
  point-to-line constraint
  problem space reduce from (x,y,\theta) to (u,\phi)
Results

## Slide 92: Inchworm Approach

## Slide 93: Self-Reference Motion Model

## Slide 94: Concertina Analogue

## Slide 95: Concertina Analogue

## Slide 96: Reference Points
Each segment a potential reference point

## Slide 97: Reference Points
Each segment a potential reference point
Old reference points used to compute new

## Slide 98: Reference Points
Each segment a potential reference point
Old reference points used to compute new
A segment becomes a reference if:
  Segment is part of an anchor
  Local joints are “stable”

## Slide 100: Motion Estimation Error

## Slide 101: Motion Estimation Error
Caused by reference points in motion

## Slide 102: Motion Estimation Error
Caused by reference points in motion
Good anchoring is key to good motion estimation

## Slide 103
Brief detour on anchoring

## Slide 104: Anchor Failure Modes
Floating references (solved)
  Locally stable but not anchored
Weak contact (minimized impact)
  Not strong anchor
Buckling (solved)
  Joint gives out under high torque
Impulse force (minimized impact)
  Sudden injection of force causes wobbling before restoring to original position
Whole body slip (open)
  Undetectable movement of whole body… no joints move
  Need accelerometer
Meta-stable anchoring (open)
  Strong in one direction but comes lose in other (funnel anchor)

## Slide 105: Anchoring
Anchoring process

## Slide 106: Anchoring
Anchoring process
  Search for amplitude

## Slide 107: Anchoring
Anchoring process
  Search for amplitude
  Joint resistance indicates contact

## Slide 108: Anchoring
Anchoring process
  Search for amplitude
  Joint resistance indicates contact
  Find snug fit but not overly stressed

## Slide 109: Anchoring
Anchoring process
  Search for amplitude
  Joint resistance indicates contact
  Find snug fit but not overly stressed
  Perform jerk test to see if secure

## Slide 110: Anchoring
Anchoring process
  Search for amplitude
  Joint resistance indicates contact
  Find snug fit but not overly stressed
  Perform jerk test to see if secure
  If not secure, start over with more segments

## Slide 111: Anchoring

## Slide 112: Current Anchoring Results
Works on variable width (within limits)
Works on smooth vs irregular surface
Works on 2-way, 3-way, 4-way junctions
When failure occurs, the 2nd or 3rd retry will succeed

## Slide 113: Results
Naive + GPAC Frame
Self-Posture + Body Frame
Pose Step + GPAC Frame (discussed later)
Shoot Step (discussed later)

## Slide 114: Mapping Problem
Actions:
  Move commands:
Sensing:
  Posture sequence:
  Posture Images:
Map Parameters:
  Poses:

## Slide 115: Poses
Pose is the position and orientation of a posture image in the posture frame
Need ways to generate
Initial condition:
  Set
  or ground truth pose.

## Slide 116: Use Overlap Inter-Pose Step
Start with X_1 given
Sense posture images
Action: ‘f’
Experience: I_1, I_2, f, I_3, I4
Solve for X_2, X_3, X_4
X_2 = overlap(X_1, I_1, I_2, d=0)
X_3 = overlap(X_1, I_1, I_3, d=+k)
X_4 = overlap(X_3, I_3, I_4, d=0)

## Slide 117: Results
Simple map example (graphic)
Problem:
  only uses last to constrain next
  does not use all history
  breaks when backtracking
  show example of breaking (graphic)

## Slide 118: Pose Graph
Try using GraphSLAM technique with poses
Use overlap step to create constraints between poses
Problem:
  depends on common feature landmarks viewable from different poses to create feature constraints
    We have NO features that act as point landmarks
  Our overlap constraints do not follow normal distribution
    Do not fit in standard GraphSLAM formulation
  How do we connect/constrain new poses to old poses without landmarks?

## Slide 119: Stable Poses

## Slide 120: Root References

## Slide 121: Pose Nodes

## Slide 122: Pose Graph

## Slide 123: Aggregate Pose Constraint
To make use of complete history of poses, we take the union of all the spatial images I_1:t situated in space at X_1:t
Compute medial axis of the union and gives us a curve that describes the shape of the environment
We define this curve to be called a “shoot”
Now we can perform localization of a new pose on the existing map
We can create constraints without mutually observable point features

## Slide 124: Aggregate Pose Constraint
Motion estimation by overlap inter-pose step
Given the estimated pose, perform ICP between new pose’s spatial curve and map’s shoot curve

## Slide 125: Aggregate Pose Constraint
Now we can perform backtracking
Featureless lengths of pipe vary in length accuracy
Bends and angles are well-formed
Results chart with single-path examples and backtracking (chart)

## Slide 126: Node in the Graph
Estimated Pose
  (X, Y, A)
Local Map

## Slide 127: Global Map
Render pose graph
  Plot local maps to estimated poses

## Slide 129: Mapping with Junctions
A shoot curve breaks down when we have a junction since there are many possible configurations for the pose to localize to
Overlap is undefined for a spatial curve that is not contained or extending the shoot
A spatial curve that does not have these properties is diverging
Overlap ICP leads to local minima
Define:
  Contained: spatial curve is contained by shoot curve
  Extension: spatial curve extends from the terminal
  Divergence: spatial curve bends away from shoot curve
  (graphics)
Alternately, we could localize the spatial curve onto the full skeleton from the union of spatial images in a junctioned environment
  However the ICP on the skeleton leads to many local minima depending on the initial condition
Such junctioned environments include 3-arm or 4-arm junctions such Y, T, and cross junctions
Junctions are not directly observable from spatial images.

## Slide 130: Mapping with Junctions
In the event of a divergence, the map representation must be extended
A new shoot is created that diverges from the original shoot whose origin is the point of divergence. The branch point
Thus the term “shoot” is like the branches of a plant.

## Slide 131: Mapping with Junctions
In the event of a pose that straddles both shoots, we localize to a curve that is a splice of the two shoots
Define shoot as
  a set of poses
  an originating shoot ID
  a shoot frame origin
  transform from parent frame to child frame
Shoot curve is dynamically generated from
  the union of the set spatial images
  compute the medial axis skeleton
  trim at the branch point
  find the longest path

## Slide 132: Mapping with Junctions
Rules:
  All shoots have parent-child relationships
  If pose overlaps multiple shoots, membership is to the junior shoot
  can have multiple membership between siblings
  Shoot curve and branch points dynamically generated from
    set of spatial images
    shoot membership
    estimated poses

## Slide 133: Mapping Process
Mapping process has 5 major stages
  Locomotion step
  Proprioceptive sensing
  Motion estimation
  Add to shoots
  Localize
Locomotion and sensing still remain the same

## Slide 134: Mapping Process
Motion estimation is augmented to include all splices of shoots for displacement.
Overlap step followed by ICP on each splice.
Select the result that has lowest cost
Evaluation function = (equation)

## Slide 135: Mapping Process
Add-to-shoots classifies a new pose to an existing shoot or determines if a new shoot needs to be created
If new spatial curve is diverging after motion estimation, then we branch and create a new shoot.
Otherwise, we proceed to next mapping step.

## Slide 136: Mapping Process
We localize on the existing shoots.
For all spliced combinations of shoots, ICP to spliced curve the pose’s spatial curve
Select best fit via evaluation function
Evaluation Function = (equation)

## Slide 137: Results
Results show the successful detection and mapping of junctions with some error
Particularly where the different arms of the junction intersect.
The angles of the junction are correct, but the arms don’t necessarily align.
Similarly, on the return to a branch arm, we cannot necessarily know if we have been to this arm before or if we need to create a new one.
It is possible to create multiple versions of the same branch.

## Slide 138: Challenges
The challenges are:
  aligning junctions (graphic)
  associating with the same junction, not duplicating branches
  false branches

## Slide 139: Branch Detection
Some evaluation is required to determine whether a new shoot needs to be made
The efficacy of the detector determines whether or not we have false positives or false negatives
Our evaluation function = K(x) (equation)
The function requires tuning and there are numerous cases where the branch evaluation will fail, regardless of tuning.

## Slide 140: Mapping with Junctions
branch condition
  extension vs. divergence
  divergence properties (discontinuity)
  curve operations

## Slide 141: Mapping Problem
Actions:
  Move commands:
Sensing:
  Posture sequence:
  Posture Images:
Map Parameters:
  Poses:
  Shoots:
  Branch Points:

## Slide 142: Probabilistic Mapping
Pose particle filter
Branch point space
Branching decision (yes/no)
Evaluation function of Poses, Branch points, Branch Decisions

## Slide 143: Probabilistic Mapping
Given that there are a number of different parameters and decisions to build the map, it is easy to build the map incorrectly
If we consider a space of possible maps, we can find the most likely map based on the robot experience
Given our definitions, find P(x|a,s) and the most likely map

## Slide 144: Probabilistic Mapping
We show how each component of th emap is represented probabilistically
  pose
  motion estimation
  localization
  shoot branch location
  multi-branch evaluation
  branch decision
  hard problems, cross and T junctions
  spatial features
  multi-junction environments

## Slide 145: Poses
Pose, represented by P(X)
  where x = (x,y,\theta)
We represent a sampling of possible poses as points on the shoot map
Each sample is individually displaced and localized

## Slide 146: Motion Estimation
Each locomotion step on each pose particle is displaced a distance with some probability
A displacement is randomly sampled from a normal distribution with mean \mu and variance \sigma
There is 10% chance that the displacement is backwards

## Slide 147: Localization
After each sample has been localized, they are evaluated for fitness and resampled
Using the localization evaluation function
(equation)

## Slide 148: Shoot Branch Location
When branching a new shoot, we cannot guarantee it is placed in the correct location.
Particularly when we are trying to correctly align the arms of a junction
If we represent the space of possible branches, then we can select the most likely after sufficient evidence has been gathered
Particularly we are interested in the joint probability distribution of P(X,B) = P(B|X)P(X)
  where P(X) can be computed by the evaluation function on each of the pose samples
  P(B|X) is the likelihood of a branch position given the current pose X
Branch positions are discretized and only the ones in the immediate vicinity of pose x are considered
For each sample pose, we evaluate 5 possible branch locations.
The configuration of the child shoot w.r.t. its parent is modified by placing its frame origin on different locations on the parent shoot curve.
Evaluation is based on the overlap consistency of the shoot skeletons and the pose’s spatial curve

## Slide 149: Multi-Branch Evaluation
In the event of proximity to multiple branch points, we must consider the joint distributions of P(B1,B2|X)
Given K states for each branch, there are K^2 combinations for a pair of branches
The number of combinations increases exponentially for every additional branch
The order of calculations is O(N*max(B*K,1)*(2+B choose 2))
  N = # of pose samples
  B = # branches
  K = # branch samples
So their complexity grows rapidly with
  the number of pose samples we have
  the number of branches under consideration
  the resolution of our branch point discretization

## Slide 150: Branch Decision
Given that our branch detection algorithm is prone to errors and that we need to resolve whether the robot has entered an existing branch or a new branch, we would also like to evaluate the space of possible branch decisions.
Given for every pose, we can decide to branch/no-branch, there are 2^t possible combinations for n poses.
We also have N pose samples that may give different results from the branch detector.
To reduce the space, we only consider the maximum likelihood sample for branch detection.
If the branch detector evaluates True, we create two maps:
  map hypothesis with the new branching shoot
  map hypothesis without the branch

## Slide 151: Branch Decision
Each separate map hypothesis is evaluated independently with its own pose and branch distributions.
In the event that a new robot pose is unable to localize to the map or the map becomes inconsistent, the map hypothesis is eliminated.
A map hypothesis becomes inconsistent when a child shoot no longer diverges from its parent.

## Slide 152: Hard Problems
Cross and T junctions
Our approach works well for Y junctions and in some cases the T junction.
However, it does not work so well for cross junctions.
In order to fully align all the branch arms of a cross junction, we need 6 complete junction postures to completely describe the junction. (graphic)
Without these postures, we can describe a junction that is incorrect but is consistent with the sensed experience
Furthermore, posture 5 and 6 do not give us different experiences from just being in a straight featureless pipe.
It is currently impossible to sense whether the robot is within a junction if it is not angled in some way
Similarly, a T-junction from the side cannot detect the junction if it goes straight through.

## Slide 153: Spatial Features
Up until this point, we have been able to build maps without landmark features or being able to directly sense a junction.
However, in order to solve the problem of observing junctions with straight postures, we must exploit some features of the spatial images
Upon inspection of spatial images within junctions, we notice swelling of the space where the walls don’t exist.
This swelling often indicates the presence of a junction.
We can build a detector for this feature, but we are finally making some strong assumptions about the width of the environment. That is, the width is some constant W.

## Slide 154: Spatial Features
We detect 3 different spatial feature from spatial images that are indicate of junctions:
  blooms: swelling at the tip
  arches: internally swelling, “arched” anchors
  bends: sudden turn of spatial curve, crest is the bend point
Using these landmark features, we now include proximity with each other in the evaluation of motion estimation, branch state, and pose localization.
Using this approach, we are able to map and align the arms of a T and cross junction with ease.
The addition of the spatial features makes mapping and aligning the other junction much more rapid.

## Slide 155: Multi-Junction Environments
We can map multi-junction environments if we assume the junction features have a minimum distance between each other
Distance is greater than twice the length of the robot posture curve.
This ensures that each junction cannot be sensed simultaneously and that features of each junction in the map cannot be mistaken for each other
This is a hard problem and we leave it for future work.

## Slide 156: Navigation
Finally, in our evaluation of whether mapping is successful, we determine if the robot can use the map to navigate with
Successful navigation means our mapping algorithm is a success for that environment
Fortunately, the shoot curves and their splices provide perfect navigation paths.
They are input to our PathFollow behavior.
Localization of the robot’s pose gives us more confidence in the robot’s location
When the robot approaches the destination point, the navigation terminates.
The maximum likelihood map state is used for navigation
If in the course of navigation, a more likely map state is found, the navigation is recomputed

## Slide 158: Particle Filter over Poses and Branch Locations

## Slide 159: Pose Particles after Localization

## Slide 160: Shoots
A single path of poses from an origin to a terminal point.
Shoots branch from other shoots

## Slide 161
 |  | Junction Types |  |  |  |  |  |  |  |  | 
 |  | T Junction from Bottom | T Junction from Side | Y junction | Right L-junction | Left L-junction | Cross Junction | Straight Pipe | Irregular Pipe | Right 60-junction | Left 60-junction
Mapping Capabilities | Forward Locomotion |  |  |  |  |  |  |  |  |  | 
 | Backtracking |  |  |  |  |  |  |  |  |  | 
 | Single Junction |  |  |  |  |  |  |  |  |  | 
 | Multi-Junctions |  |  |  |  |  |  |  |  |  | 
 | Navigation |  |  |  |  |  |  |  |  |  | 
 | Legend |  |  |  |  |  |  |  |  |  | 
 | Success |  |  |  |  |  |  |  |  |  | 
 | Partial Success |  |  |  |  |  |  |  |  |  | 
 | Not yet demonstrated |  |  |  |  |  |  |  |  |  | 
 | N/A |  |  |  |  |  |  |  |  |  | 

## Slide 162: Conclusion
Absence of external sensors
  use proprioception to build spatial awareness
Use any robot so long as it has lots of joints and known geometry
Spatial images give incomplete information
  Obstacle and extent of reach are identical
We determined that spatial curves derived from the medial axis computation give the most usable environmental data for building maps

## Slide 163: Conclusion
To estimate motion from locomotion, we developed a constrained estimated based on the confined structure of the environment and the assumption that consecutive poses will always be partially overlapping
In the event of a junction, we detect it if a pose’s spatial curve diverges from the shoot curve
Junctions are represented in the map by branching new child shoots
In junction environments, motion estimation and localization are accomplished by comparing their operations against all spliced curves and selecting the splice with the best evaluated utility function
The maximum likelihood map is found by modeling the state space of maps and evaluating multiple options that are most probable

## Slide 164: Conclusion
N possible poses are evaluated each with K^2 possible branch configurations.
A new map hypothesis is created for each branch decision
T and cross junctions were found to be challenging with no landmark features
We found and exploited spatial features as landmarks for the presence of junctions
Multi-junction environments are capable of being mapped so long as the junctions are spaced far enough apart to prevent incorrect feature associations
We evaluate our approach as successful because we can use the generated map to navigate robot path following